## Slide 1: CSDS 451: Designing High Performant Systems for AI
Lecture 2
8/28/2025
Sanmukh Kuppannagari
sanmukh.kuppannagari@case.edu
https://sanmukh.research.st/
Case Western Reserve University

## Slide 2: Outline
Why Performance Modeling?
Processor Memory Architectures
  Basic Execution Model
  Memory System Modeling

## Slide 3: Outline
Why Performance Modeling?
Processor Memory Architectures
  Basic Execution Model
  Memory System Modeling

## Slide 4: Performance Modeling
Identifying important parameters that determine the performance of an algorithm mapped to the platform
  Algorithm – Parallel algorithm that we have designed
  Platform – The target hardware on which we wish to run the parallel algorithm
Identifying equations that govern the performance

## Slide 5: Why Performance Modeling?
Serial Code
For to
  =
  If break
  Else: Do work()
What are the important parameters?
What are the equations governing the performance of the algorithm?

## Slide 6: Why Performance Modeling?
Serial Code
For to
  =
  If break
  Else: Do work()
What are the important parameters?
What are the equations governing the performance of the algorithm?
M,N
Min{log M,N}

## Slide 7: Why Performance Modeling?
Complexity Analysis of Serial Algorithms
  Bubble sort (n^3) vs Merge sort (n log n)
  Parameter that determine performance: input size
  Equations governing performance – complexity of the algorithm
Provide understanding of bottlenecks and what to optimize
Do not provide actual implementation estimates
  Quick sort vs Merge sort ???

## Slide 8: Parallel Algorithm Performance Modeling
Performance is platform dependent
Different platforms -> different parameters
Different platforms -> different equations governing performance

## Slide 9: Targeted Platforms
Processor-Memory Architecture
  CPUs, GPUs
Systolic Array Architecture
  TPUs, Tensor Cores
Clusters
  HPC

## Slide 10: Why Performance Modeling?
Most importantly, to get a mental model of how the algorithm you are designing runs on the hardware, without going into specifics of the hardware.
Parallel programs can be notoriously hard to reason about
Simple performance models, even if not accurate, can help us get clarity on execution and aid in debugging

## Slide 11: Outline
Why Performance Modeling?
Processor Memory Architectures
  Basic Execution Model
  Memory System Modeling

## Slide 12: Basic Execution Model Fetch-Execute
A simple view
Fetch
Execute
Memory
Processor
Memory access = 1 cycle for any location
Execution = 1 cycle
Parameters:

## Slide 13: Basic Execution Model Calculating Algorithm Performance
Consider the following computation
C[i] = *
to
to
What is the above operation?

## Slide 14: Basic Execution Model Calculating Algorithm Performance
Consider the following computation
C[i] = *
to
to
What is the above operation? Matrix-Vector Multiplication

## Slide 15: Matrix Vector Multiplication
C[i] = *
0,0
0,1
0,2
1,0
1,1
1,1
0
1
2
X
0
1
C
A
B
=
M
N
N
M

## Slide 16: Basic Execution Model Calculating Algorithm Performance
C[i] = *
Decompose the equation into two types of instructions
Fetch: Read from memory or Write to memory
Execute: Arithmetic/Logical Operation
Memory
Processor

## Slide 17: Basic Execution Model Calculating Algorithm Performance
C[i] = *
RA: Read A[i][k]
RB: Read B[k]
M: Res <- Mult A[i][k]*B[k]
RC: Read C[i]
A: Add C[i] + Res
S: Store C[i]
Memory
Processor

## Slide 18: Basic Execution Model Calculating Algorithm Performance
C[i] = *
RA: Read A[i][k]
RB: Read B[k]
M: Res <- Mult A[i][k]*B[k]
RC: Read C[i]
A: Add C[i] + Res
S: Store C[i]
Memory
Processor
Assume we are storing these in a local memory (such as registers) in the processor

## Slide 19: Basic Execution Model
Assumptions
No limit on the local memory
  Putting a limit may require us to use a different set of instructions
Addition and Multiplications are each single cycle operations
  Not necessarily true in modern architectures

## Slide 20: Basic Execution Model Calculating Algorithm Performance
C[i] = *
RA: Read A[i][k]
RB: Read B[k]
M: Res <- Mult A[i][k]*B[k]
RC: Read C[i]
A: Add C[i] + Res
S: Store C[i]
6 cycles per entry of A
Total Time for the entire matrix = ??

## Slide 21: Basic Execution Model Calculating Algorithm Performance
C[i] = *
RA: Read A[i][k]
RB: Read B[k]
M: Res <- Mult A[i][k]*B[k]
RC: Read C[i]
A: Add C[i] + Res
S: Store C[i]
6 cycles per entry of A
Total Time for the entire matrix = 6*M*N cycles

## Slide 22: Basic Execution Model
Assume Processor is running at 2 GHz
Total time (in seconds) to execute Matrix-Vector Multiplication as per Basic Execution Model
???
Memory
Processor
2 Ghz

## Slide 23: Basic Execution Model
Assume Processor is running at 2 GHz
Total time to execute Matrix-Vector Multiplication as per Basic Execution Model
seconds
Memory
Processor
2 Ghz

## Slide 24: Basic Execution Model: Limitations
Does not account for memory transfer latencies
Does not account for differences in the number of cycles in various arithmetic operations
  Multiplication usually requires more cycles than addition

## Slide 25: Basic Execution Model: Uses
It will be a part of more complicated models that we will study next
With modern pipelined architectures, 1 cycle per execute operation is not a bad assumption

## Slide 26: Outline
Why Performance Modeling?
Processor Memory Architectures
  Basic Execution Model
  Memory System Modeling

## Slide 27: Memory System
System performance (execution time) depends on the “rate” at which data can be accessed by the program
64
P
M (DRAM)
Updated Execution Model
Latency: Time to receive the first word since the fetch instruction
Bandwidth: Rate of data transfer = bitwidth of the interconnect x frequency
Execute – 1 cycle
Fetch – Latency + Data size/bandwidth cycles

## Slide 28: Memory System
System performance (execution time) depends on the “rate” at which data can be accessed by the program
64
P
M (DRAM)
Updated Execution Model
Latency: Time to receive the first word since the fetch instruction
Bandwidth: Rate of data transfer = bitwidth of the interconnect x frequency
Execute – 1 cycle
Fetch – Latency + Data size/bandwidth cycles

## Slide 29: Memory System
Latency: Every fetch request requires some setup operation in memory before it can actually start transferring the data
Bandwidth: Once the data starts transferring, it can continuously transfer without any interruptions depending upon the speed of the interconnect, as long as it is contiguous
Fetch request: Given me 10 data elements starting at location 0
0

## Slide 30: Memory System
Read A[0-31]
Latency: 10 cycles
Bandwidth: 8 data elements per cycle (assuming 8 bits/data element)
Number of cycles to finish the read operation?
64
P
M (DRAM)

## Slide 31: Memory System
Read A[0-31]
Latency: 10 cycles
Bandwidth: 8 data elements per cycle (assuming 8 bits/data element)
Number of cycles to finish the read operation? 10 + 4 = 14 cycles
64
P
M (DRAM)

## Slide 32: Memory System
Read A[0-31], A[32-63], A[64-95]
Latency: 10 cycles
Bandwidth: 8 data elements per cycle (assuming 8 bits/data element)
Number of cycles to finish the read operation?
64
P
M (DRAM)

## Slide 33: Memory System
Read A[0-31], A[32-63], A[64-95]
Latency: 10 cycles
Bandwidth: 8 data elements per cycle (assuming 8 bits/data element)
Number of cycles to finish the read operation? 10 + 4 + 10 + 4 + 10 + 4 = 42 cycles
64
P
M (DRAM)

## Slide 34: Memory System
Read A[0-95]
Latency: 10 cycles
Bandwidth: 8 data elements per cycle (assuming 8 bits/data element)
Number of cycles to finish the read operation?
64
P
M (DRAM)

## Slide 35: Memory System
Read A[0-95]
Latency: 10 cycles
Bandwidth: 8 data elements per cycle (assuming 8 bits/data element)
Number of cycles to finish the read operation? 10 + 12 = 22 cycles
64
P
M (DRAM)

## Slide 36: Memory System
By fetching the entire 96 words in a single go, we saved 20 cycles
Prefetching:
  If you know what data your algorithm needs to access beforehand (not as easy as it sounds)
  Prefetch it to save on latency
(Note: above 20 cycles is based on a simple model, in reality, it is difficult to exactly calculate the savings, but we do see substantial savings)

## Slide 37: Memory System
System performance (execution time) depends on the “rate” at which data can be accessed by the program
64
P
M (DRAM)
Updated Execution Model
Latency: Time to receive the first word since the fetch instruction
Bandwidth: Rate of data transfer = bitwidth of the interconnect x frequency
Execute – 1 cycle
Fetch – Latency + Data size/bandwidth cycles

## Slide 38: Memory System
Latency: Every fetch request requires some setup operation in memory before it can actually start transferring the data
Bandwidth: Once the data starts transferring, it can continuously transfer without any interruptions depending upon the speed of the interconnect, as long as it is contiguous
Fetch request: Given me 10 data elements starting at location 0
0

## Slide 39: Memory System: Modeling
Performance will be measured in terms of “System Performance Metric”
Number of “useful computations” performed per second
Useful computation – arithmetic computations such as Add, Mult, etc.
  Does not include memory fetching time in calculations

## Slide 40: System Performance Metric
FLOPs – Floating Point Operations Per Second
Number of useful “floating point” operations in a second
GFLOPs – Giga (1024) Floating Point Operations Per Second
Note: Unless explicitly specified, we will use 64 bit floating point as data type for performance modeling in this class.
We will call each data element as a word

## Slide 41: System Performance Metric
1024 read operations
For every two read operations, we perform one add operation.
All the operations mentioned above take a total of 10 seconds.
What is the system performance?

## Slide 42: System Performance Metric
1024 read operations
For every two read operations, we perform one add operation.
All the operations mentioned above take a total of 10 seconds.
What is the system performance? 512 Floating point operations in 10 seconds

## Slide 43: System Performance Metric
1024 read operations
For every two read operations, we perform one add operation.
All the operations mentioned above take a total of 10 seconds.
What is the system performance? 51.2 FLOPs

## Slide 44: System Performance Metric
1024 read operations
For every two read operations, we perform one add operation.
All the operations mentioned above take a total of 10 seconds.
What is the system performance? 0.05 GFLOPs

## Slide 45: Memory System Modeling
64
P
M (DRAM)
Processor
2 Ghz (0.5 ns per cycle)
Memory
Memory Latency = 10 ns (20 cycles)
Bandwidth = 64 bits at 1 GHz
(64 Gbits/sec or 8 GB/sec) or
(64 bits in every 2 processor cycles)

## Slide 46: Memory System Modeling
We will consider three metrics:
  Peak Performance
  Sustained Performance (best case)
  Sustained Performance (worst case)
Actual obtained performance on the hardware should be somewhere in between Sustained Performance (worst case) and Peak Performance
  If not, there was some error in modeling or the implementation of the algorithm
  It can be higher or lower than the Sustained Performance (best case), this information governs what optimizations to use

## Slide 47: Memory System Modeling: Peak Performance
Captures the Raw Computer power of the processor (memory not considered)
Peak Performance = Clock Rate X Num ops per cycle
= 2 (Ghz) x 1 (ops/cycle)
= 2 Giga Ops per Second
If Floating point ops = 2 GFLOPs (Giga Floating Point Operations per second)

## Slide 48: Memory System Modeling: Peak Performance
Captures the Raw Computer power of the processor (memory not considered)
Peak Performance = Clock Rate X Num ops per cycle
= 2 (Ghz) x 1 (ops/cycle)
= 2 Giga Ops per Second
If Floating point ops = 2 GFLOPs (Giga Floating Point Operations per second)
For multiple processors/GPUs, this number will change

## Slide 49: Memory System Modeling: Sustained Performance (Worst Case)
Each fetch takes: Latency + (data size = 1)/bandwidth latency number of cycles
C[i] = *
RA: Read A[i][k]
RB: Read B[k]
M: Res <- Mult A[i][k]*B[k]
RC: Read C[i]
A: Add C[i] + Res
S: Store C[i]
Latency
Latency
1
Latency
1
Latency

## Slide 50: Memory System Modeling: Sustained Performance (Worst Case)
Each fetch takes: Latency + (data size = 1)/bandwidth latency number of cycles
Example: When Prefetching is not used
  In reality, the data size will be cache line length, but we are simplifying the model here
  Also, the sophisticated caching mechanisms in modern architectures ensure the performance is not this bad

## Slide 51: Memory System Modeling: Sustained Performance (Worst Case)
64
P
M (DRAM)
Processor
2 Ghz (0.5 ns per cycle)
Memory
Memory Latency = 10 ns (20 cycles)
Bandwidth = 64 bits at 1 GHz
(64 Gbits/sec or 8 GB/sec) or
(64 bits in every 2 processor cycles)
Can you calculate the Sustained Performance (worst case) in GFLOPs for the entire matrix?

## Slide 52: Memory System Modeling: Sustained Performance (Worst Case)
Fetch = ??
Execute = ??
Total time (per each loop over ) =
Number of Operations (per each loop over ) = ??
Performance: ?? GFLOPs

## Slide 53: Memory System Modeling: Sustained Performance (Worst Case)
Fetch = 10 ns
Execute = 0.5 ns
Total time (per each loop over ) = ns
Number of Operations (per each loop over ) = 2
Performance: 2/41 ns = 0.048 GFLOPs

## Slide 54: Memory System Modeling: Sustained Performance (Best Case)
In Sustained Performance (worst case), we were fetching one word at a time.
  Separate fetch instructions
  Each instruction incurring latency
Sustained Performance (best case): Assume data is contiguously stored
  Single fetch can be performed
  Assume latency is 0
64
P
M (DRAM)

## Slide 55: Memory System Modeling: Sustained Performance (Best Case)
How can the latency be 0?
Data prefetching: Processor initiates data transfer request way before the data is actually needed
Predicting data prefetching parameters using ML is a hot research topic: https://scholar.google.com/scholar?as_ylo=2018&q=data+prefetching+machine+learning&hl=en&as_sdt=0,36
We will not cover in this class

## Slide 56: Memory System Modeling: Sustained Performance (Best Case)
Each fetch takes: Latency (=0) + data size/bandwidth data size/bandwidth
C[i] = *
RA: Read A[i][k]
RB: Read B[k]
RC: Read C[i]
M: Res <- Mult A[i][k]*B[k]
A: Add C[i] + Res
S: Store C[i]
Single Fetch at rate of bandwidth
1
Single Fetch at the rate of bandwidth
1

## Slide 57: Memory System Modeling: Sustained Performance (Best Case)
Each fetch takes: Latency (=0) + data size/bandwidth data size/bandwidth
C[i] = *
RA: Read A[i][k]
RB: Read B[k]
RC: Read C[i]
M: Res <- Mult A[i][k]*B[k]
A: Add C[i] + Res
S: Store C[i]
Time in ns??
Time in ns??
Time in ns??
Time in ns??

## Slide 58: Memory System Modeling: Sustained Performance (Best Case)
64
P
M (DRAM)
Processor
2 Ghz (0.5 ns per cycle)
Memory
Memory Latency = 10 ns (20 cycles)
Bandwidth = 64 bits at 1 GHz
(64 Gbits/sec or 8 GB/sec) or
(64 bits in every 2 processor cycles)
Can you calculate the Sustained Performance (best case) in GFLOPs for the entire matrix?

## Slide 59: Memory System Modeling: Sustained Performance (Worst Case)
Each fetch takes: Latency (=0) + data size/bandwidth data size/bandwidth
C[i] = *
RA: Read A[i][k]
RB: Read B[k]
RC: Read C[i]
M: Res <- Mult A[i][k]*B[k]
A: Add C[i] + Res
S: Store C[i]
3 ns
0.5 ns
1 ns
0.5 ns

## Slide 60: Memory System Modeling: Sustained Performance (Best Case)
Total time (per loop over ) = ns
Number of Operations (per loop over ) = 2
Performance: 2/5 ns = 0.4 GFLOPs
Notes
  Again we assumed no limit on local memory of processor
  Also, note how we reordered the read instructions to maximize bandwidth use

## Slide 61: System Performance Metrics
2 Gflops/s
0.4 Gflops/s
0.048 Gflops/s
Sustained Worst Case
Latency dominant
Sustained Best Case
Latency Hidden
Memory bandwidth dominant
Peak Performance
Compute Only
Actual System Performance
Latency Hiding Mechanisms
Efficient Bandwidth Utilization

## Slide 62: Memory System: Conclusion
A simple model to perform “pen and paper” calculations to analyze an algorithm
Compare various algorithms in a similar spirit as complexity analysis
Get a mental model of the algorithm execution to potentially find better optimizations

## Slide 63: Memory System: Conclusion
Ungraded HW assignment 1: Can you create a simple code to perform these calculations? (May help you in your assignments later)

## Slide 64: Next Class
9/2 Lecture 3 – Processor-Memory Architecture II
  Memory Optimizations,
  Processor Memory Architectures with Cache
  Blocked Matrix Multiplication

## Slide 65: Thank You
Questions?
Email: sanmukh.kuppannagari@case.edu