## Slide 1: CSDS 451: Designing High Performant Systems for AI
Lecture 3
9/2/2025
Sanmukh Kuppannagari
sanmukh.kuppannagari@case.edu
https://sanmukh.research.st/
Case Western Reserve University

## Slide 2: Outline
Processor Memory Architectures
  Memory Optimizations to Improve Performance
  Processor Memory Architectures with Cache
  Blocked Matrix Multiplication

## Slide 3: Announcements
PA 0 due this Thursday
WA 1 will be out Thursday
  Will cover topics till lecture 6
TA Information and Office hours will be posted by tonight

## Slide 4: Outline
Processor Memory Architectures
  Memory Optimizations to Improve Performance
  Processor Memory Architectures with Cache
  Blocked Matrix Multiplication
Modeling GPU Architectures

## Slide 5: Recall: Memory System
System performance (execution time) depends on the “rate” at which data can be accessed by the program
64
P
M (DRAM)
Updated Execution Model
Latency: Time to receive the first word since the fetch instruction
Bandwidth: Rate of data transfer = bitwidth of the interconnect x frequency
Execute – 1 cycle
Fetch – Latency + Data size/bandwidth cycles
With DRAM access latency of 100s of cycles,
Need latency hiding mechanisms

## Slide 6: Recall: System Performance Metrics
2 Gflops/s
0.4 Gflops/s
0.048 Gflops/s
Sustained Worst Case
Latency dominant
Sustained Best Case
Latency Hidden
Memory bandwidth dominant
Peak Performance
Compute Only
Actual System Performance
Latency Hiding Mechanisms
Efficient Bandwidth Utilization

## Slide 7: System Performance Metrics
If actual performance less than Sustained Performance (best case)
  Latency not fully hidden – employ optimizations to hide latency
  Memory bandwidth not fully utilized – employ optimizations to improve bandwidth
If actual performance more than Sustained Performance (best case) but less than Peak Performance
  Latency is hidden, memory bandwidth is fully utilized
  Need to perform more computations on the fetched data (may or may not be possible depending upon the algorithm)

## Slide 8: Techniques to Improve Application Performance
Compute Parallelization
  Decompose tasks to enable concurrent processing (we will discuss later in this course)
Memory Optimizations
  Optimizations addressing latency
  Optimizations targeted toward maximizing bandwidth utilization
  Optimizations that maximize computations on the fetched data (in other words, reduce the amount of data transfers that need to occur)

## Slide 9: Learning Objectives
Understand the optimizations addressing latency
Understand the optimizations targeted toward maximizing bandwidth utilization
Understand optimizations that reduce the amount of data transfer and maximize computations

## Slide 10: #1 Optimizations Targeting Latency
Key ideas
  Latency of a single data item cannot be reduced due to physical constraints
  Try to hide the latency by doing some independent useful work such as
    Data transfer
    computations
0
0.5
1
Read
ns
-19
Read Request
Time of data arrival
Latency

## Slide 11: #1 Optimizations Targeting Latency
Latency Hiding using data transfers
  Avoid per data latency (Sustained Performance (worst case)) by multiple requests in sequence
  After an initial latency, data arrives continuously
0
0.5
1
Read
ns
-19
Read Request
Times of data arrival
Latency
1.5
2
2.5
Read
Read
3

## Slide 12: #1 Optimizations Targeting Latency
Latency hiding using data transfers
  In practice, consecutive requests to random locations leads to addition memory device specific latencies
  Accessing sequential data leads to higher performance
0
0.5
1
Read
ns
-19
Read Request
Times of data arrival
Latency
1.5
2
2.5
Read
Read
3

## Slide 13: #1 Optimizations Targeting Latency
Latency hiding using data transfers
  Key takeaway for this course: data transfers of sequential datastructures (such as arrays) leads to streaming data transfers, i.e., data transfers where latencies for the subsequent data items is hidden.
0
0.5
1
Read
ns
-19
Read Request
Times of data arrival
Latency
1.5
2
2.5
Read
Read
3
Recall last class: Fetch request format: read 100 elements starting at location 0.

## Slide 14: #1 Optimizations Targeting Latency
Latency hiding using computation
Several mechanisms exist
  Prefetching
  Thread switching
  …
Mostly provided by the hardware/operating system
Prefetching is provided as an option to algorithm developer – we will revisit later in the class

## Slide 15: #1 Optimizations Targeting Latency
Optimizations that you can use in your algorithms
Store the data in arrays in a sequential manner, in the order in which the algorithm is expected to access it (Data layout optimizations that we will discuss later in today’s lecture)
Prefetch the data into the local memory before the computations begin (Will discuss later today and in GPU programming lectures)
Requires Cache a local on-chip memory where data can be stored till all the computations are performed

## Slide 16: #2 Optimizations to Improve Bandwidth
Key Idea
  Memory systems have wide “buses” – bunch of wires that transfer data from memory to processors
  Bandwidth is essentially buswidth X clock frequency
  Pack the bus as much as possible in each cycle to transfer more data
P
M (DRAM)
64
P
M (DRAM)
Should pack 64 bits in each cycle to maximize bandwidth

## Slide 17: #2 Optimizations to Improve Bandwidth
In Practice
  Accessing sequential data leads to better packing
  Memories usually have much larger bitwidth than 64 bits
    Nvidia A100’s memory has 5120 bit (615 bytes) wide bus.
P
M (DRAM)
64
P
M (DRAM)
Should pack 64 bits in each cycle to maximize bandwidth

## Slide 18: #2 Optimizations to Improve Bandwidth
Optimizations that you can use in your algorithms
Store the data in arrays in a sequential manner (again, data layout optimizations like we will discuss later in this lecture)
When fetching, try to fetch as much data as possible in a single go (again, prefetching that we will discuss in GPU programming lectures)
Requires Cache a local on-chip memory where data can be stored till all the computations are performed

## Slide 19: Memory Optimizations #1 and #2
Similar strategies
Should help us achieve Sustained Performance (best case)
  Theoretically. In practice, getting 0 latency or 100% bandwidth utilization is very difficult, so performance may still be lower.
Now the next step to improve performance further will be to maximize the computations performed on the fetched data
  We will call this – optimizations to maximize data reuse (we reuse fetched data for computations as much as possible)
  Maximizing data reuse implies reducing data transfers

## Slide 20: #3 Optimizations to Maximize Data Reuse
Objective is to maximize the computations that can be performed on the data once fetched
Most of the memory optimizations employed in application acceleration research fall under this category

## Slide 21: #3 Optimizations to Maximize Data Reuse
0,0
0,1
0,2
1,0
1,1
1,1
0
1
2
X
0
1
C
A
B
=
M
N
N
M
Algorithms typically perform multiple operations on various data items

## Slide 22: #3 Optimizations to Maximize Data Reuse
0,0
0,1
0,2
1,0
1,1
1,1
0
1
2
X
0
1
C
A
B
=
M
N
N
M
Data Reuse: How many times (on average) an input/output location is used

## Slide 23: #3 Optimizations to Maximize Data Reuse
0,0
0,1
0,2
1,0
1,1
1,1
0
1
2
X
0
1
C
A
B
=
M
N
N
M
Data Reuse for B???

## Slide 24: #3 Optimizations to Maximize Data Reuse
0,0
0,1
0,2
1,0
1,1
1,1
0
1
2
X
0
1
C
A
B
=
M
N
N
M
Data Reuse for B: times

## Slide 25: #3 Optimizations to Maximize Data Reuse
0,0
0,1
0,2
1,0
1,1
1,1
0
1
2
X
0
1
C
A
B
=
M
N
N
M
Data Reuse for A???

## Slide 26: #3 Optimizations to Maximize Data Reuse
0,0
0,1
0,2
1,0
1,1
1,1
0
1
2
X
0
1
C
A
B
=
M
N
N
M
Data Reuse for A: time

## Slide 27: #3 Optimizations to Maximize Data Reuse
0,0
0,1
0,2
1,0
1,1
1,1
0
1
2
X
0
1
C
A
B
=
M
N
N
M
Data Reuse for A+B+C???

## Slide 28: #3 Optimizations to Maximize Data Reuse
0,0
0,1
0,2
1,0
1,1
1,1
0
1
2
X
0
1
C
A
B
=
M
N
N
M
Data Reuse for A+B+C :

## Slide 29: #3 Optimizations to Maximize Data Reuse
How do we make sure that each data item of B is fetched just once and used times?

## Slide 30: #3 Optimizations to Maximize Data Reuse
How do we make sure that each data item of B is fetched just once and used times?
Effectively use Cache a local on-chip memory where data can be stored till all the computations are performed
Before we can “effectively” use cache, lets first understand how to model it

## Slide 31: Execution Model with Cache
64
DRAM
C
Processor
Cache
Small (16 MB)
Fast (2 GHz)
4 GB
Fetch_Memory – Latency + Data size/bandwidth
Fetch_Cache – 1 cycle
Execute – 1 cycle
Bandwidth = 64 bits at 1 GHz
(64 Gbits/sec or 8 GB/sec) or
(64 bits in every 2 processor cycles) or 1 word in 1 ns
Read/Write from DRAM to/from Cache
Basic Execution Model
Latency: 10 ns

## Slide 32: Execution Model with Cache
Assumptions
Fetch_Memory: DRAM <-> Cache
Processor has a limited number of registers, say 3-4
  You can decide what “limited” means
  Enough such that you don’t need complicated code
  But not so large that you do not require cache anymore

## Slide 33: Execution Model with Cache Calculating Algorithm Performance
C[i] = *
RMA: Read A into cache
RMB: Read B into cache
{ //repeat M*N times
  RA: Read A[i][k] into processor
  RB: Read B[k] into processor
  M: Res <- Mult A[i][k]*B[k]
  RC: Read C[i] into processor
  A: Add C[i] + Res
  S: Store C[i] into cache
}
SMC: Store C into DRAM

## Slide 34: Execution Model with Cache Calculating Algorithm Performance
C[i] = *
RMA: Read A into cache
RMB: Read B into cache
{ //repeat M*N times
  RA: Read A[i][k] into processor
  RB: Read B[k] into processor
  M: Res <- Mult A[i][k]*B[k]
  RC: Read C[i] into processor
  A: Add C[i] + Res
  S: Store C[i] into cache
}
SMC: Store C into DRAM
This is prefetching which avoids the latency of fetching each M*N RA, RB, and S operations

## Slide 35: Execution Model with Cache Calculating Algorithm Performance
C[i] = *
RMA: Read A into cache
RMB: Read B into cache
{ //repeat M*N times
RA: Read A[i][k] into processor
RB: Read B[k] into processor
M: Res <- Mult A[i][k]*B[k]
RC: Read C[i] into processor
A: Add C[i] + Res
S: Store C[i] into cache
}
SMC: Store C into DRAM
??
??
??
??

## Slide 36: Execution Model with Cache Calculating Algorithm Performance
C[i] = *
RMA: Read A into cache
RMB: Read B into cache
{ //repeat M*N times
RA: Read A[i][k] into processor
RB: Read B[k] into processor
M: Res <- Mult A[i][k]*B[k]
RC: Read C[i] into processor
A: Add C[i] + Res
S: Store C[i] into cache
}
SMC: Store C into DRAM
10 + MN ns
10 + N ns
3MN ns
10 + N ns

## Slide 37: Execution Model with Cache
System Performance: ??

## Slide 38: Execution Model with Cache
System Performance:
2MN useful operations
Time (ns): 30 + 3MN + MN + 2N
System Performance (GFLOPs): 2MN/(30 + 4MN + 2N)

## Slide 39: Execution Model with Cache
Recall
Peak Performance: 2 GFLOPs
Sustained Performance (best case): 0.4 GFLOPs
Sustained Performance (worst case): 0.048 GFLOPs
Sustained Performance (with cache): 2MN/(30 + 4MN + 2N)

## Slide 40: Execution Model with Cache
Recall
Peak Performance: 2 GFLOPs
Sustained Performance (best case): 0.4 GFLOPs
Sustained Performance (worst case): 0.048 GFLOPs
Sustained Performance (with cache): 2MN/(4MN)
  For large MN

## Slide 41: Execution Model with Cache
Recall
Peak Performance: 2 GFLOPs
Sustained Performance (best case): 0.4 GFLOPs
Sustained Performance (worst case): 0.048 GFLOPs
Sustained Performance (with cache): 0.5 GFLOPs
  For large MN

## Slide 42: Execution Model with Cache
Ungraded HW assignment (may include as a question in WA 1, or even better, in the exam)
Why is the performance marginally better than Sustained Performance (best case)? Why not lower or significantly better?

## Slide 43: Memory Bound Applications
Why is the performance still significantly lower than peak performance?
Peak Performance: 2 GFLOPs
Sustained Performance (best case): 0.4 GFLOPs
Sustained Performance (with cache): 0.5 GFLOPs

## Slide 44: Memory Bound Applications
Why is the performance still significantly lower than peak performance?
Time (ns): 30 + 3MN + MN + 2N 4MN
Time spent on Computation: MN
Time spent on Memory Operations: 3MN
Performance is limited by how fast data can be fed to the processors – Memory boundedness
  We will look at optimizations to maximize data reuse in next class which can be used to optimize these types of applications

## Slide 45: Cache Limitations
In practice, cache size is limited
Previously fetched data is evicted from cache, if no space.
We need to carefully design our algorithms to obtain best performance using cache
Enable effective utilization of cache to maximize data reuse and minimize data transfers

## Slide 46: Optimizations to Enable Effective Utilization of Cache
#1 Data Layout Optimizations
#2 Algorithm Reordering to Maximize Data Reuse

## Slide 47: #1 Data Layout Optimization
A in Memory
Cache
Need to Fetch elements 2 at a time to cache.
Each Fetch_Memory – Latency + data size/bandwidth

## Slide 48: #1 Data Layout Optimization
A in Memory
Cache
Need to Fetch elements 2 at a time to cache.
Each Fetch_Memory – Latency + data size/bandwidth

## Slide 49: #1 Data Layout Optimization
A in Memory
Cache
Need to Fetch elements 2 at a time to cache.
Each Fetch _Memory – Latency + data size/bandwidth

## Slide 50: #1 Data Layout Optimization
A in Memory
Cache
Need to Fetch elements 2 at a time to cache.
Each Fetch _Memory – Latency + data size/bandwidth

## Slide 51: #1 Data Layout Optimization
A in Memory
Cache
Need to Fetch elements 2 at a time to cache.
Each Fetch _Memory – Latency + data size/bandwidth

## Slide 52: #1 Data Layout Optimization
A in Memory
Cache
Algorithm access Pattern: 0, 2, 4, 6, 8, 1, 3, 5, 7
0
1
2
3
4
5
6
7
8

## Slide 53: #1 Data Layout Optimization
A in Memory
Cache
Algorithm access Pattern: 0, 2, 4, 6, 8, 1, 3, 5, 7
Number of Fetch_Memory Needed: ??
0
1
2
3
4
5
6
7
8

## Slide 54: #1 Data Layout Optimization
A in Memory
Cache
Algorithm access Pattern: 0, 2, 4, 6, 8, 1, 3, 5, 7
Number of Fetch_Memory Needed: 9
0
1
2
3
4
5
6
7
8

## Slide 55: #1 Data Layout Optimization
A in Memory
Cache
Algorithm access Pattern: 0, 2, 4, 6, 8, 1, 3, 5, 7
Number of Fetch_Memory Needed: ??
??
??
??
??
??
??
??
??
??

## Slide 56: #1 Data Layout Optimization
A in Memory
Cache
Algorithm access Pattern: 0, 2, 4, 6, 8, 1, 3, 5, 7
Number of Fetch_Memory Needed: 5
0
2
4
6
8
1
3
5
7

## Slide 57: #1 Data Layout Optimization
A in Memory
Cache
Or Change Algorithm access Pattern: 0, 1,2,3,4,5,6,7,8
Number of Fetch_Memory Needed: 5
0
1
2
3
4
5
6
7
8

## Slide 58: #1 Data Layout Optimization
Objective: Ensure sequential access to data stored in memory by,
  Either, storing data in the right format
  Or, reordering computations (access pattern of program)

## Slide 59: #1 Data Layout Optimization
Storing a 2-dimemsional array in memory
Row major order
Column major order
0
-1
-1
0
0
0
-1
-1
…
…
Memory
Memory
Map
Map

## Slide 60: #1 Data Layout Optimization
For k = 1 to n
  For i = 1 to n
    C[i] <- A[i][k] + B[k] + C[i]
  Assume is stored in row major order
Row major order
0
-1
-1
0
…
Column major access pattern
Access pattern of the program
Data Layout
Data Access not sequential
Each read of A[i][k] will incur latency

## Slide 61: #1 Data Layout Optimization
Assume is stored in row major order
For i = 1 to m
  For k = 1 to n
    C[i] <- A[i][k] + B[k] + C[i]
Row major access pattern
Access pattern of the program
Data Layout
Data Access sequential
Read A[i][k] at the rate of bandwidth

## Slide 62: #1 Data Layout Optimization
Alternate Solution: Store A in Column major order
Access pattern of the program
Data Layout
Data Access sequential
Read A[i][k] at the rate of bandwidth

## Slide 63: #1 Data Layout Optimization: Summary
We should align the layout of the data in the memory to match with the access pattern of the algorithm
  Simple N-D row/column major layout should be sufficient for most purposes
Access patterns may change over iterations of the algorithm
  For example, 2D FFT
  Algorithm designers sometimes employ dynamic data layout changing mechanisms, if the overheads are justified
We will not discuss dynamic data layout optimizations in this class

## Slide 64: #2 Improving Data Reuse
Our objective is to reduce the number of data transfers of input and output
If a data element is used multiple times, try to reorder the algorithm such that all its uses are “temporally” close to each other
We will discuss this in the next class when we look at how to reorder matrix multiplication algorithm to improve data reuse

## Slide 65: Next Class
9/4 Lecture 4 – Blocked MM for improving data reuse, Modeling GPU Architectures

## Slide 66: Thank You
Questions?
Email: sanmukh.kuppannagari@case.edu