## Slide 1: CSDS 451: Designing High Performant Systems for AI
Lecture 4
9/4/2025
Sanmukh Kuppannagari
sanmukh.kuppannagari@case.edu
https://sanmukh.research.st/
Case Western Reserve University

## Slide 2: Outline
Processor Memory Architectures
  Blocked Matrix Multiplication
Modeling GPU Architectures
Data Parallel Programming

## Slide 3: Outline
Processor Memory Architectures
  Blocked Matrix Multiplication
Modeling GPU Architectures
Data Parallel Programming

## Slide 4: System Performance Metrics
If actual performance less than Sustained Performance (best case)
  Latency not fully hidden – employ optimizations to hide latency
  Memory bandwidth not fully utilized – employ optimizations to improve bandwidth
If actual performance more than Sustained Performance (best case) but less than Peak Performance
  Latency is hidden, memory bandwidth is fully utilized
  Need to perform more computations on the fetched data (may or may not be possible depending upon the algorithm)

## Slide 5: Techniques to Improve Application Performance
Compute Parallelization
  Decompose tasks to enable concurrent processing (we will look at it later in today’s lecture and in the next lecture)
Memory Optimizations
  Optimizations addressing latency
  Optimizations targeted toward maximizing bandwidth utilization
  Optimizations that maximize computations on the fetched data (in other words, reduce the amount of data transfers that need to occur)

## Slide 6: #1 Optimizations Targeting Latency
Optimizations that you can use in your algorithms
Store the data in arrays in a sequential manner, in the order in which the algorithm is expected to access it (Data layout optimizations)
Prefetch the data into the local memory before the computations begin
Requires Cache a local on-chip memory where data can be stored till all the computations are performed

## Slide 7: #2 Optimizations to Improve Bandwidth
Optimizations that you can use in your algorithms
Store the data in arrays in a sequential manner
When fetching, try to fetch as much data as possible in a single go
Requires Cache a local on-chip memory where data can be stored till all the computations are performed

## Slide 8: Memory Optimizations #1 and #2
Similar strategies
Should help us achieve Sustained Performance (best case)
  Theoretically. In practice, getting 0 latency or 100% bandwidth utilization is very difficult, so performance may still be lower.
Now the next step to improve performance further will be to maximize the computations performed on the fetched data
  We will call this – optimizations to maximize data reuse (we reuse fetched data for computations as much as possible)
  Maximizing data reuse implies reducing data transfers

## Slide 9: Execution Model with Cache
64
DRAM
C
Processor
Cache
Small (16 MB)
Fast (2 GHz)
4 GB
Fetch_Memory – Latency + Data size/bandwidth
Fetch_Cache – 1 cycle
Execute – 1 cycle
Bandwidth = 64 bits at 1 GHz
(64 Gbits/sec or 8 GB/sec) or
(64 bits in every 2 processor cycles) or 1 word in 1 ns
Read/Write from DRAM to/from Cache
Basic Execution Model
Latency: 10 ns

## Slide 10: Memory Bound Applications
Why is the performance still significantly lower than peak performance?
Time (ns): 30 + 3MN + MN + 2N 4MN
Time spent on Computation: MN
Time spent on Memory Operations: 3MN
Performance is limited by how fast data can be fed to the processors – Memory boundedness
  We will look at optimizations to maximize data reuse in next class which can be used to optimize these types of applications

## Slide 11: Cache Limitations
In practice, cache size is limited
Previously fetched data is evicted from cache, if no space.
We need to carefully design our algorithms to obtain best performance using cache
Enable effective utilization of cache to maximize data reuse and minimize data transfers

## Slide 12: Optimizations to Enable Effective Utilization of Cache
#1 Data Layout Optimizations
#2 Algorithm Reordering to Maximize Data Reuse

## Slide 13: #1 Data Layout Optimization: Summary
We should align the layout of the data in the memory to match with the access pattern of the algorithm
  Simple N-D row/column major layout should be sufficient for most purposes
Access patterns may change over iterations of the algorithm
  For example, 2D FFT
  Algorithm designers sometimes employ dynamic data layout changing mechanisms, if the overheads are justified
We will not discuss dynamic data layout optimizations in this class

## Slide 14: #2 Improving Data Reuse
Our objective is to reduce the number of data transfers of input and output
If a data element is used multiple times, try to reorder the algorithm such that all its uses are “temporally” close to each other
Blocked Matrix Multiplication

## Slide 15: Matrix Multiplication
B
A
C
N
N
N
N
N
N

## Slide 16: Matrix Matrix Multiplication
C[i][j] = A[i][k] * B[k][j]
0,0
0,1
0,2
1,0
1,1
1,1
0,0
1,0
2,0
X
0,0
1,0
C
A
B
=
M
K
K
M
0,1
1,1
2,1
0,1
1,1
N
N

## Slide 17: Matrix Multiplication
Cache Size -
Definition:
Data Reuse Factor (for an algorithm): Number of Computations/Number of data transfers
Can be used to determine the effectiveness of an algorithm

## Slide 18: Matrix Multiplication
Data Reuse Factor, with infinite cache
Fetch matrix A - data transfers
Fetch matrix B - data transfers
Fetch matrix C - data transfers
Compute C = computation operations
Save C back to memory - data transfers
Data Reuse Factor:

## Slide 19: Matrix Multiplication
Data Reuse Factor, with infinite cache
Fetch matrix A - data transfers
Fetch matrix B - data transfers
Fetch matrix C - data transfers
Compute C = computation operations
Save C back to memory - data transfers
Data Reuse Factor:

## Slide 20: Naïve Matrix Multiplication
B
A
C
N
N
N
N
N
N
Basic three loop Algorithm:
For each i,j of C
  Fetch row i of A
  Fetch column j of B
  Perform dot product to produce C[i][j]
Assume Cache size

## Slide 21: Naïve Matrix Multiplication
B
A
C
N
N
N
N
N
N
Basic three loop Algorithm:
For each i,j of C
  Fetch row i of A
  Fetch column j of B
  Perform dot product to produce C[i][j]
Assume Cache size
Data reuse factor = ??

## Slide 22: Naïve Matrix Multiplication
B
A
C
N
N
N
N
N
N
Basic three loop Algorithm:
For each i,j of C
  Fetch row i of A
  Fetch column j of B
  Perform dot product to produce C[i][j]
Assume Cache size
Data reuse factor = ??
Matrix A – Fetch 1 time ( data transfers)
Matrix B – Fetch N times ( data transfers)
Matrix C – Fetch 1 times ( data transfers)

## Slide 23: Naïve Matrix Multiplication
B
A
C
N
N
N
N
N
N
Basic three loop Algorithm:
For each i,j of C
  Fetch row i of A
  Fetch column j of B
  Perform dot product to produce C[i][j]
Assume Cache size
Data reuse factor =
Matrix A – Fetch 1 time ( data transfers)
Matrix B – Fetch N times ( data transfers)
Matrix C – Fetch 1 times ( data transfers)

## Slide 24: Block Matrix Multiplication
Key Idea: Partition matrices A/B/C into size blocks
Blocks denoted as Ab[1:][1:]/ Bb[1:][1:]/ Cb[1:][1:]
Cb[i][j] = BlockedMM(Ab[i][:], Bb[:][j])
For to
  Fetch Ab[i][k], Bb[k][j]
  Matrix Multiply Ab[i][k], Bb[k][j] and Accumulate Cb[i][j]
i,j]
i,:]
:,j]

## Slide 25: Block Matrix Multiplication
i,j]
i,:]
:,j]
Perform Matrix Multiplication of these two blocks

## Slide 26: Block Matrix Multiplication
i,j]
i,:]
:,j]
Perform Matrix Multiplication of these two blocks

## Slide 27: Block Matrix Multiplication
i,j]
i,:]
:,j]
Perform Matrix Multiplication of these two blocks

## Slide 28: Block Matrix Multiplication
i,j]
i,:]
:,j]
Perform Matrix Multiplication of these two blocks

## Slide 29: Block Matrix Multiplication
Data Reuse Factor =

## Slide 30: Block Matrix Multiplication
For each Cb[i][j]

## Slide 31: Block Matrix Multiplication
For each Cb[i][j]
Fetch Ab[i][k], Bb[k][j], – how many data transfers?

## Slide 32: Block Matrix Multiplication
For each Cb[i][j]
Fetch Ab[i][k], Bb[k][j], –
Block Size

## Slide 33: Block Matrix Multiplication
For each Cb[i][j]
Fetch Ab[i][k], Bb[k][j], –
Computations for Ab[i][k], Bb[k][j], - ?? computations
Block Size
Range of k

## Slide 34: Block Matrix Multiplication
For each Cb[i][j]
Fetch Ab[i][k], Bb[k][j], –
Computations for Ab[i][k], Bb[k][j], - computations
Range of k
Computations per block

## Slide 35: Block Matrix Multiplication
For each Cb[i][j]
Fetch Ab[i][k], Bb[k][j], –
Computations for Ab[i][k], Bb[k][j], - computations
Store Cb[i][j] - data transfers

## Slide 36: Block Matrix Multiplication
For each Cb[i][j]
Fetch Ab[i][k], Bb[k][j], –
Computations for Ab[i][k], Bb[k][j], - computations
Store Cb[i][j] - data transfers

## Slide 37: Block Matrix Multiplication
For each Cb[i][j]
Fetch Ab[i][k], Bb[k][j], –
Computations for Ab[i][k], Bb[k][j], - computations
Store Cb[i][j] - data transfers
Number of Cb[i][j] blocks - ??

## Slide 38: Block Matrix Multiplication
For each Cb[i][j]
Fetch Ab[i][k], Bb[k][j], –
Computations for Ab[i][k], Bb[k][j], - computations
Store Cb[i][j] - data transfers
Number of Cb[i][j] blocks -

## Slide 39: Block Matrix Multiplication
Data Reuse Factor:
Total Computations -
Total data transfers – transfers
Data Reuse Factor:

## Slide 40: Block Matrix Multiplication
Data Reuse Factor:
Total Computations -
Total data transfers – transfers
Data Reuse Factor:

## Slide 41: Block Matrix Multiplication
Data Reuse Factor:
Total Computations -
Total data transfers – transfers
Data Reuse Factor:
Data Reuse Factor: = for
For naïve case:
For infinite cache:

## Slide 42: Block Matrix Multiplication – Things to Notice
No change in total computations – still
In naïve MM – A fetched once, B fetched times
In Blocked MM – A fetched times, B fetched times
We balanced the data reuse between A and B to achieve a better overall reuse

## Slide 43: Block Matrix Multiplication – Things to Notice
In practice, Matrices A and B can be of different sizes,
Optimal block sizes may be different for A and B.
  May not even be square blocks – tiles
Tiled Matrix Multiplication – Use rectangular blocks instead of square
Automatic Tuning of Tile sizes – An important way to optimize matrix operations in practice
  ATLAS - https://math-atlas.sourceforge.net/
  Jack Dongarra – Turing Award, 2021
  “For his pioneering contributions to numerical algorithms and libraries that enabled high performance computational software to keep pace with exponential hardware improvements for over four decades”

## Slide 44: Ungraded HW Assignment
Consider our memory system with cache model
Consider the naïve and blocked matrix multiplication algorithms
Model them on the platform and compare performance (Sustained Performance (with cache))
Change or assume any input or cache sizes as needed to simplify calculations and improve understanding

## Slide 45: Outline
Processor Memory Architectures
  Blocked Matrix Multiplication
Modeling GPU Architectures
Data Parallel Programming

## Slide 46: CPU + GPU Heterogeneity

## Slide 47: Modeling GPU Architectures
DRAM
C
C
C
GPU Architecture
A collection of Symmetric Multi-Processor (SMP)
Each SMP – Processor/Memory Architecture with Cache with multiple processors running in lock step
SPMD – Single Program Multiple Data Paradigm

## Slide 48: Modeling GPU Architectures
DRAM
C
C
C
Global Memory
This is where we transfer data from the CPU
Nvidia A100 – 80 GB; Nvidia H100 – 96 GB
Global Memory; VRAM; …

## Slide 49: Modeling GPU Architectures
DRAM
C
C
C
Symmetric Multi Processor
An array of compute cores working in lockstep manner
Have access to a shared cache
Each compute core can access any location in the shared cache, even if the location was written by a different compute core
Symmetric Multi-Processor; …

## Slide 50: Modeling GPU Architectures
DRAM
C
C
C
Threads and Blocks
Threads run on compute cores

## Slide 51: Modeling GPU Architectures
DRAM
C
C
C
Threads and Blocks
Threads run on compute cores
Collection of threads is called a block
Blocks run on Symmetric Multi-Processor (SMP)

## Slide 52: Modeling GPU Architectures
DRAM
C
C
C
Threads and Blocks
Threads run on compute cores
Collection of threads is called a block
Blocks run on Symmetric Multi-Processor (SMP)
Each block associated with a BlockID
  Each thread associated with a ThreadID
  Unique within a block, but threads across different blocks can have same ThreadID
BlockID = 0
BlockID = 1
BlockID = k
0
1
0
1
0
1

## Slide 53: Modeling GPU Architectures
DRAM
C
C
C
Number of Blocks can be (in fact should be) greater than the number of SMPs
Number of threads per block need not be equal to the number of compute cores per SMP
  It is good to have it as a multiple though
We will discuss these considerations when we discuss GPU programming later
For now, assume the simple model above.
  Blocks
  Threads per block
0
1
0
1
0
1

## Slide 54: GPU Model Calculating Algorithm Performance
C[i] = *
A not so good algorithm
  BlockID responsible for computing
  ThreadID computes the product of and store into Temp[k]
  ThreadID computes the sum and stores into C[i]

## Slide 55: GPU Model Calculating Algorithm Performance
BlockID 0

## Slide 56: GPU Model Calculating Algorithm Performance
BlockID 1

## Slide 57: GPU Model Calculating Algorithm Performance
BlockID

## Slide 58: GPU Model Calculating Algorithm Performance
ThreadID 0

## Slide 59: GPU Model Calculating Algorithm Performance
ThreadID 1

## Slide 60: GPU Model Calculating Algorithm Performance
ThreadID

## Slide 61: GPU Model Calculating Algorithm Performance
ThreadID

## Slide 62: GPU Model Calculating Algorithm Performance
ThreadID

## Slide 63: GPU Model Calculating Algorithm Performance
ThreadID

## Slide 64: GPU Model Calculating Algorithm Performance
ThreadID

## Slide 65: GPU Model Calculating Algorithm Performance
C[i] = *
A not so good algorithm
  BlockID responsible for computing
  ThreadID computes the product of and store into Temp[k]
  ThreadID computes the sum and stores into C[i]
Why is this not so good?

## Slide 66: GPU Model Calculating Algorithm Performance
C[i] = *
A not so good algorithm
  BlockID responsible for computing
  ThreadID computes the product of and store into Temp[k]
  ThreadID computes the sum and stores into C[i]
Why is this not so good? When adding, all other threads are idling

## Slide 67: GPU Model Calculating Algorithm Performance
C[i] = *
Assume
In thread: bid, tid
RMA: Read A[bid][tid] into cache
RMB: Read B[tid] into cache
Syncthreads()
RA: Read A[bid][tid] into processor
RB: Read B[tid] into processor
M: Temp[tid] <- Mult A[bid][tid]*B[tid]
syncthreads()
In thread 0
{ Repeat for iter = 1 to times
A: Temp[0] = Temp[0] + T[iter]
C[bid] = Temp[0]
}
SMC: Store C[bid] into DRAM

## Slide 68: GPU Model Calculating Algorithm Performance
C[i] = *
Assume
In thread: bid, tid
RMA: Read A[bid][tid] into cache
RMB: Read B[tid] into cache
Syncthreads()
RA: Read A[bid][tid] into processor
RB: Read B[tid] into processor
M: Temp[tid] <- Mult A[bid][tid]*B[tid]
syncthreads()
In thread 0
{ Repeat for iter = 1 to times
A: Temp[0] = Temp[0] + T[iter]
C[bid] = Temp[0]
}
SMC: Store C[bid] into DRAM
Notice how the code is bid, tid dependent.

## Slide 69: GPU Model Calculating Algorithm Performance
C[i] = *
Assume
In thread: bid, tid
RMA: Read A[bid][tid] into cache
RMB: Read B[tid] into cache
Syncthreads()
RA: Read A[bid][tid] into processor
RB: Read B[tid] into processor
M: Temp[tid] <- Mult A[bid][tid]*B[tid]
syncthreads()
In thread 0
{ Repeat for iter = 1 to times
A: Temp[0] = Temp[0] + T[iter]
C[bid] = Temp[0]
}
SMC: Store C[bid] into DRAM
Also, notice how each thread performs the same computation but on different data (SPMD)

## Slide 70: GPU Model Calculating Algorithm Performance
C[i] = *
Assume
In thread: bid, tid
RMA: Read A[bid][tid] into cache
RMB: Read B[tid] into cache
Syncthreads()
RA: Read A[bid][tid] into processor
RB: Read B[tid] into processor
M: Temp[tid] <- Mult A[bid][tid]*B[tid]
syncthreads()
In thread 0
{ Repeat for iter = 1 to times
A: Temp[0] = Temp[0] + T[iter]
C[bid] = Temp[0]
}
SMC: Store C[bid] into DRAM
All threads in the block collectively bring data into the shared cache - prefetching

## Slide 71: GPU Model Calculating Algorithm Performance
C[i] = *
Assume
In thread: bid, tid
RMA: Read A[bid][tid] into cache
RMB: Read B[tid] into cache
Syncthreads()
RA: Read A[bid][tid] into processor
RB: Read B[tid] into processor
M: Temp[tid] <- Mult A[bid][tid]*B[tid]
syncthreads()
In thread 0
{ Repeat for iter = 1 to times
A: Temp[0] = Temp[0] + T[iter]
C[bid] = Temp[0]
}
SMC: Store C[bid] into DRAM
A synchronization step is needed for all the threads to finish fetching

## Slide 72: GPU Model Calculating Algorithm Performance
C[i] = *
Assume
In thread: bid, tid
RMA: Read A[bid][tid] into cache
RMB: Read B[tid] into cache
Syncthreads()
RA: Read A[bid][tid] into processor
RB: Read B[tid] into processor
M: Temp[tid] <- Mult A[bid][tid]*B[tid]
syncthreads()
In thread 0
{ Repeat for iter = 1 to times
A: Temp[0] = Temp[0] + T[iter]
C[bid] = Temp[0]
}
SMC: Store C[bid] into DRAM
Computation in parallel and synchronization

## Slide 73: GPU Model Calculating Algorithm Performance
C[i] = *
Assume
In thread: bid, tid
RMA: Read A[bid][tid] into cache
RMB: Read B[tid] into cache
Syncthreads()
RA: Read A[bid][tid] into processor
RB: Read B[tid] into processor
M: Temp[tid] <- Mult A[bid][tid]*B[tid]
syncthreads()
In thread 0
{ Repeat for iter = 1 to times
A: Temp[0] = Temp[0] + T[iter]
C[bid] = Temp[0]
}
SMC: Store C[bid] into DRAM
Thread 0 performs the sum.
All other threads idle (in practice they still execute the instructions, but the outputs are invalidated)

## Slide 74: GPU Model Calculating Algorithm Performance
C[i] = *
Assume
In thread: bid, tid
RMA: Read A[bid][tid] into cache
RMB: Read B[tid] into cache
Syncthreads()
RA: Read A[bid][tid] into processor
RB: Read B[tid] into processor
M: Temp[tid] <- Mult A[bid][tid]*B[tid]
syncthreads()
In thread 0
{ Repeat for iter = 1 to times
A: Temp[0] = Temp[0] + T[iter]
C[bid] = Temp[0]
}
SMC: Store C[bid] into DRAM
Ungraded HW assignment: Calculate the system performance metrics for this code.
Assume hardware parameters for memory system with cache that we used in last class. Assume syncthreads is 0 cycles.
Q: What is the new peak performance?
Q: What is the sustained performance you obtain here?

## Slide 75: GPU Model
Think in terms of what each block computes, and what each thread within a block computes
Each thread on the GPU executes the same instructions on different data
We need to rethink our algorithms in terms of the above
We will look at a few more GPU algorithms in Lecture 6

## Slide 76: Outline
Processor Memory Architectures
  Blocked Matrix Multiplication
Modeling GPU Architectures
Data Parallel Programming

## Slide 77: Data Parallelism
Key Idea:
  Partition data into chunks – to ensure load balancing
  Assign tasks to each partition so that they can proceed concurrently
Note: data parallelism doesn’t mean each task “need” to perform exact same computations
  Usually it is true
SPMD (Single Program Multiple Data) is a special case of data parallelism where same “program” is run on different data

## Slide 78: Data Parallelism - Approaches
#1 Partition Output data
  Each task is responsible for computing an output partition
Output

## Slide 79: Data Parallelism - Approaches
#1 Partition Output data
  Each task is responsible for computing an output partition
Output

## Slide 80: Data Parallelism - Approaches
#1 Partition Output data
  Each task is responsible for computing an output partition
Output

## Slide 81: Data Parallelism - Approaches
#1 Partition Output data
  Useful when partitions of output can be computed independently of each other
  Example: Blocked Matrix Multiplication
Output

## Slide 82: Data Parallelism – Approaches
#1 Partition Output data
  Matrix Multiplication
Input data maybe shared
Output data distinct

## Slide 83: Data Parallelism - Approaches
#2 Partition Input data
  Each task is responsible for performing “all” operations on the partition
Input

## Slide 84: Data Parallelism - Approaches
#2 Partition Input data
  Each task is responsible for performing “all” operations on the partition
Input

## Slide 85: Data Parallelism - Approaches
#2 Partition Input data
  Each task is responsible for performing “all” operations on the partition
Input

## Slide 86: Data Parallelism - Approaches
#2 Partition Input data
  Tasks can either directly produce the final output
  Or produce intermediate output which require another set of tasks to produce the final output
Input

## Slide 87: Data Parallelism - Approaches
#2 Partition Input data
  Suitable when outputs cannot be independently computed
    Example: Aggregation functions, Hashing, …
Input

## Slide 88: Data Parallelism - Approaches
#2 Partition Input data
Problem: Constructing a Hash Table
Inputs: a set of keys in the Universe
Output: mapping of each key to an index in

## Slide 89: Data Parallelism - Approaches
#2 Partition Input data
Problem: Constructing a Hash Table
Can we do data parallelism based on output partitioning?

## Slide 90: Data Parallelism - Approaches
#2 Partition Input data
Problem: Constructing a Hash Table
Can we do data parallelism based on output partitioning?
  Yes, but
  What if the partition has no keys mapped to it – idle processor
  What if the partition has too many keys mapped to it – load balancing issue
  Does each processor need to look into the entire dataset? – wasteful computations

## Slide 91: Data Parallelism - Approaches
#2 Partition Input data
  Divide the keys equally among processors

## Slide 92: Data Parallelism - Approaches
#2 Partition Input data
  Pros: no wasteful computations, no idle processors

## Slide 93: Data Parallelism - Approaches
#2 Partition Input data
  Cons: May need to do synchronization
    Load balancing issues – Processors that see more conflicts will complete later than processors that see fewer conflicts

## Slide 94: Data Parallelism - Approaches
#3 Partition both Input and Output data
Lets revisit the output partitioning in hash tables in detail

## Slide 95: Data Parallelism - Approaches
Cons: wasteful computations
  Notice: Hash value of each key computed times

## Slide 96: Data Parallelism - Approaches
Pros: No synchronization

## Slide 97: Data Parallelism - Approaches
#3 Partition both inputs and outputs
  For each input output pair, assign a processor

## Slide 98: Data Parallelism - Approaches
Assuming input partitions, output partitions, we have

## Slide 99: Data Parallelism - Approaches
# hash computations per key value???
# Processors that may conflict??

## Slide 100: Data Parallelism - Approaches
# hash computations per key value - in output only partitioning
# Processors that may conflict - in input only partitioning

## Slide 101: Next Class
9/9 Lecture 4 – Access to CWRU HPC; Writing DNN pipelines in pytorch
9/11 Lecture 5 – Data Parallel Algorithms on GPUs; Task Parallelism

## Slide 102: Thank You
Questions?
Email: sanmukh.kuppannagari@case.edu